## Slide 1: NR500-EA
V1.1

## Slide 2: spec

## Slide 3
 | Feature | Description
 | Form Factor | 5G Router
Interface | Network | 1*1000Mbps LAN
 | Voice | 1*RJ11(optional)
 | SIM | 2FF or 4FF(DUAL SIM OPTIONAL)
 | Button | Reset/WPS/Battery level/Power
 | Battery | 7.4V(2000mAh X 2) (optional) or 7.4V(5000mAh X 2) (optional)
 | External antenna | TS9 (optional)
 | TypeC | Firmware upgrade
 | DC | Input voltage: 12V-1.5A
Solution | 5G Module | RG500U-EA
 | 5G Module processor | UNISOC UDX710
 | 5G Module Processor parameters | Dual-core ARM Cortex-A55 procesador 1.35GHz
 | WIFI Module | FC06E
 | WIFI Module processor | Qualcomm 2064
Envionment | Operating temperature | -20 to 60° C
 | Storage temperature | -40 to 85° C

## Slide 4
5G/4G/3G | 3GPP Release | 5G NR (3GPP Release 15)
 | 5G Modulation | DL 256QAM, UL 256QAM
 | 4G Modulation | DL QPSK、16QAM、64QAM、256QAM, UL QPSK、16QAM、64QAM
 | 3G Modulation | QPSK、16QAM、64QAM
 | Max. transmitter Power | WCDMA B1/B2/B5/B8：Class 3 (24 dBm +1/-3 dB) LTE B1/B2/B3/B4/B5/B8/B20/B38/B40/B41/B66：Class 3 (23 dBm±2.7 dB) LTE B28：Class 3 (23 dBm +2.7/-3.2 dB) LTE B41 HPUE：Class 2 (26 dBm ±2.7 dB) 5G NR n1/n3/n5/n7/n8/n20/n38/n40/n41：Class 3 (23 dBm ±2 dB) 5G NR n28：Class 3 (23 dBm +2/-2.5 dB) 5G NR n77/n78/n79：Class 3 (23 dBm +2/-3 dB) 5G NR n41/n78/n79 HPUE：Class 2 (26 dBm +2/-3 dB)
 | Band | 5G NR NSA n1/ 3/ 7/ 38/ 40/ 41/ 77/ 78/ 79
 |  | 5G NR SA n1/ 3/ 5/ 7/ 8/ 20/ 28/ 38/ 40/ 41/ 71/ 77/ 78/ 79(n5 n71 optional)
 |  | LTE-FDD B1/ 2/ 3/ 4/ 5/ 7/ 8/ 20/ 28A/ 28B/ 66
 |  | LTE-TDD B38/ 40/ 41
 |  | WCDMA B1/B2/B5/B8
 | LTE Feature | Max：CA：DL 3CC，UL 2CC FDD：DL Cat 12，UL Cat 13 TDD：DL Cat 12，ULCat 13
 |  | Support1.4/3/5/10/15/20 MHz bandwidth
 |  | DL support2 × 2 MIMO
 |  | Max：DL 600 MbpsUL 150 Mbps
 | UMTS Feature | Support DC-HSDPA HSDPA HSUPA HSPA+ WCDMA
 |  | Max：DL 42.2 MbpsUL11Mbps
 | 5G NR Feature | DL 4 × 4 MIMO：n1/ 3/ 7/ 38/ 40/ 41/ 77/ 78/ 79 UL 2 × 2 MIMO：n38/ 40/ 41/ 77/ 78/ 79 DL 2 × 2 MIMO：n5/ 8/ 20/ 28/ 71(n5 n71 optional)NSA：MAX DL 2.6 Gbps，MAX UL 650 Mbps SA：MAX DL 2 Gbps，MAX UL 1 Gbps
 | Feature | Description

## Slide 5
WLAN | WIFI antenna | Internal antenna
 | Modulation | DBPSK/DQPSK/CCK/BPSK/QPSK/QAM
 | WiFi protocol | IEEE 802.11 a/b/g/n/ac/ax
 | Frequency | 2.4 GHz WLAN: 2.400–2.4835 GHz 5 GHz WLAN: 5.150–5.850 GHz
 | Bandwidth | 2.4G 20MHz/40MHz 5G 20MHz/40MHz/80MHz
 | Rate | 1774.5Mbps data rate (2 × 2 + 2 × 2 11ax DBS)
 | 2.4G Max. transmitter power | 802.11b/1Mbps 21dbm
 |  | 802.11g/54Mbps 19dbm
 |  | 802.11n/HT40 MCS7 18dbm
 |  | 802.11ax/HE40 MCS11 17dbm
 | 5G Max. transmitter power | 802.11a/54Mbps 18dbm
 |  | 802.11n/HT40 MCS7 18dbm
 |  | 802.11ac/VHT80 MCS9 17dbm
 |  | 802.11ax/HE80 MCS11 16.5dbm
 | Feature | Description

## Slide 6
Software | Language | English
 | Wizard | Supported
 | Device info | CPU Usaage/Memory Usage/Online time/Runtime/UUID/software version
 | Network info | IMEI/IMSI/ICCID/RSRP/RSRQ/RSSI/SINR/PCID/EARFCN/Frequency
 | DHCP server | Supported
 | DHCP client list | Supported
 | APN Setting | Supported
 | Network Lock | Supported
 | Band Lock | Supported
 | PCI Lock | Supported
 | PIN Management | Supported
 | DHCP Client | Supported
 | WIFI mac filter | White list and Black list
 | WIFI Broadcast | Supported
 | Hidden WIFI signal | Supported
 | WPS | Supported
 | WIFI Security Type | WPA-PSK/WPA2-PSK
 | SMS | Supported
 | Traffic statistics | Supported
 | NTP | Supported
 | Reboot Schedule | Supported
 | Flow setting | Supported
 | Sim card Switch | Supported (optional)
 | system log | Supported
 | system upgrade | Local upgrade/FOTA
 | Reboot and Reset | Supported
 | Signal bar | Supported (WEBUI)
 | Tr069 | Supported
 | Login Account Settings | Supported
 | Feature | Description

## Slide 7: CA Combination

## Slide 8
CA Combination | 3GPP Status | No. of CC | Region | UL | ULCA | DL 4 × 4 MIMO | Spreadsheet Version
CA_1A-1A | 3GPP | 2DL | Australia, France | 1A | - | - | V1.0
CA_1A-20A | 3GPP | 2DL | UK, Spain, Germany, Italy, Switzerland | 1A, 20A | - | - | V1.0
CA_1A-28A | 3GPP | 2DL | Australia, France, Germany, Italy, Japan, Netherlands, Switzerland, Saudi, Taiwan | 1A, 28A | - | - | V1.0
CA_1A-38A | 3GPP | 2DL | Taiwan | 1A | - | - | V1.0
CA_1A-3A | 3GPP | 2DL | Australia, Brazil, China Mainland, Hong Kong, Japan, Korea, Singapore, Taiwan, UK, Saudi, Vietnam | 1A, 3A | - | - | V1.0
CA_1A-40A | 3GPP | 2DL | Australia, Hong Kong, Saudi | 1A | - | - | V1.0
CA_1A-41A | 3GPP | 2DL | Japan, Saudi | 1A | - | - | V1.0
CA_1A-5A | 3GPP | 2DL | China Mainland, Korea | 1A, 5A | - | - | V1.0
CA_1A-7A | 3GPP | 2DL | Australia, Hong Kong, Korea, Singapore, Taiwan, UK | 1A, 7A | - | - | V1.0
CA_1A-8A | 3GPP | 2DL | China Mainland, Hong Kong, Japan, Korea, Singapore, | 1A, 8A | - | - | V1.0
CA_1C | 3GPP | 2DL | . | 1A | 1C | - | V1.0
CA_3A-20A | 3GPP | 2DL | UK, Spain, Germany, Italy, Switzerland | 3A, 20A | - | - | V1.0
CA_3A-28A | 3GPP | 2DL | Australia, Brazil, Japan, Taiwan, Saudi | 3A, 28A | - | - | V1.0
CA_3A-3A | 3GPP | 2DL | Australia, Brazil, Hong Kong, US, Saudi, Taiwan | 3A | - | - | V1.0
CA_3A-40A | 3GPP | 2DL | Australia, Hong Kong, Saudi | 3A | - | - | V1.0
CA_3A-41A | 3GPP | 2DL | Japan | 3A | - | - | V1.0
CA_3A-5A | 3GPP | 2DL | China Mainland, Korea | 3A, 5A | - | - | V1.0
CA_3A-7A | 3GPP | 2DL | Australia, Brazil, Hong Kong, Korea, Singapore, Taiwan, UK | 3A, 7A | - | - | V1.0
CA_3A-8A | 3GPP | 2DL | Hong Kong, Japan, Singapore, Taiwan | 3A, 8A | - | - | V1.0
CA_3C | 3GPP | 2DL | Australia, China Mainland, Singapore, Korea, UK, Saudi | 3A | 3C | - | V1.0
CA_5A-40A | 3GPP | 2DL | Australia | 5A | - | - | V1.0
CA_5A-5A | 3GPP | 2DL | US | 5A | - | - | V1.0
CA_5A-7A | 3GPP | 2DL | Canada, Korea, Mexico | 5A, 7A | - | - | V1.0
CA_5B | 3GPP | 2DL | US | 5A | 5B | - | V1.0
CA_7A-20A | 3GPP | 2DL | UK, Spain, Germany, Italy, Switzerland | 7A, 20A | - | - | V1.0
CA_7A-28A | 3GPP | 2DL | Argentina, Australia, Brazil, Chile, Peru, Taiwan | 7A, 28A | - | - | V1.0
CA_7A-40A |  | 2DL |  | 7A | - | - | V1.0
CA_7A-8A | 3GPP | 2DL | Australia, Germany, Hong Kong, Singapore, Taiwan | 7A, 8A | - | - | V1.0
CA_7B | 3GPP | 2DL | Australia, Canada | 7A | - | - | V1.0
CA_7C | 3GPP | 2DL | Australia, Canada, Mexico, Peru, UK | 7A | 7C | - | V1.0
CA_8A-38A | 3GPP | 2DL | Taiwan | 8A | - | - | V1.0
CA_8A-40A | 3GPP | 2DL | Hong Kong | 8A | - | - | V1.0
CA_8A-41A | 3GPP | 2DL | . | 8A | - | - | V1.0
CA_8B | 3GPP | 2DL | . | 8A | 8B | - | V1.0
CA_20A-38A | 3GPP | 2DL | . | 20A | - | - | V1.0
CA_20A-41A | 3GPP | 2DL | Saudi | 20A | - | - | V1.0
CA_28A-40A | 3GPP | 2DL | Australia, Saudi | 28A | - | - | V1.0
CA_28A-41A | 3GPP | 2DL | Japan | 28A | - | - | V1.0
CA_28C | 3GPP | 2DL | . | 28A | - | - | V1.0

## Slide 9
CA_38C | 3GPP | 2DL | Switzerland | 38A | 38C | - | V1.0
CA_40A-40A | 3GPP | 2DL | . | 40A | - | - | V1.0
CA_40C | 3GPP | 2DL | Australia, China Mainland, Hong Kong, Saudi | 40A | 40C | - | V1.0
CA_41A-41A | 3GPP | 2DL | Mexico, US | 41A | - | - | V1.0
CA_41C | 3GPP | 2DL | China Mainland, Japan, US | 41A | 41C | - | V1.0
CA_66A-66A | 3GPP | 2DL | Australia, France | 66A | - | - | V1.3
CA_4A-7A | 3GPP | 2DL | Australia, France, Germany, Italy, Japan, Netherlands, Switzerland, Saudi, Taiwan | 4A,7A | - | - | V1.3
CA_5A-7A | 3GPP | 2DL | Taiwan | 5A,7A | - | - | V1.3
CA_4A-5A | 3GPP | 2DL | Australia, Brazil, China Mainland, Hong Kong, Japan, Korea, Singapore, Taiwan, UK, Saudi, Vietnam | 5A,4A | - | - | V1.3
CA_5A-66A | 3GPP | 2DL | China Mainland, Korea | 66A,5A | - | - | V1.3
CA_2A-4A | 3GPP | 2DL | China Mainland, Hong Kong, Japan, Korea, Singapore, | 2A,4A | - | - | V1.3
CA_2A-7A | 3GPP | 2DL | . | 2A,7A |  | - | V1.3
CA_2C | 3GPP | 2DL | Australia, Brazil, Hong Kong, US, Saudi, Taiwan | 2A | 2C | - | V1.3
CA_2A-28A | 3GPP | 2DL | Australia, Hong Kong, Saudi | 2A,28A | - | - | V1.3
CA_4A-28A | 3GPP | 2DL | Japan | 4A,28A | - | - | V1.3
CA_28A-38A | 3GPP | 2DL | Australia, Brazil, Hong Kong, Korea, Singapore, Taiwan, UK | 28A | - | - | V1.3
CA_2A-38A | 3GPP | 2DL | Hong Kong, Japan, Singapore, Taiwan | 2A | - | - | V1.3
CA_7A-7A | 3GPP | 2DL | Australia, China Mainland, Singapore, Korea, UK, Saudi | 7A |  | - | V1.3
CA_1A-28A-40A | 3GPP | 3DL | Australia, Saudi | 1A, 28A | - | - | V1.0
CA_1A-3A-20A | 3GPP | 3DL | Spain, Germany, Italy, Switzerland, UAE, UK | 1A, 3A, 20A | - | - | V1.0
CA_1A-3A-28A | 3GPP | 3DL | Australia, Japan, Taiwan, Saudi | 1A, 3A, 28A | - | - | V1.0
CA_1A-3A-38A | 3GPP | 3DL | Singapore, Taiwan | 1A, 3A | - | - | V1.0
CA_1A-3A-40A | 3GPP | 3DL | Australia, Hong Kong, Saudi, Vietnam | 1A, 3A | - | - | V1.0
CA_1A-3A-41A | 3GPP | 3DL | Japan | 1A, 3A | - | - | V1.0
CA_1A-3A-5A | 3GPP | 3DL | China Mainland, Korea | 1A, 3A, 5A | - | - | V1.0
CA_1A-3A-7A | 3GPP | 3DL | Australia, Hong Kong, Korea, Singapore, Taiwan, UK | 1A, 3A, 7A | - | - | V1.0
CA_1A-3A-8A | 3GPP | 3DL | China Mainland, Hong Kong, Japan, Korea, Singapore, | 1A, 3A, 8A | - | - | V1.0
CA_1A-3C | 3GPP | 3DL | Australia, China Mainland, Singapore, Korea, UK, Saudi | 1A, 3A | 3C | - | V1.0
CA_1A-40C | 3GPP | 3DL | Hong Kong, Saudi | 1A | - | - | V1.0
CA_1A-41C | 3GPP | 3DL | Japan | 1A | - | - | V1.0
CA_1A-7A-20A | 3GPP | 3DL | France, Finland, Germany, Spain, Switzerland, Sweden | 1A, 7A, 20A | - | - | V1.0
CA_1A-7A-28A | 3GPP | 3DL | Australia, Taiwan | 1A, 7A, 28A | - | - | V1.0
CA_1A-7A-40A |  | 3DL |  | 1A, 7A | - | - | V1.0
CA_1A-7A-8A | 3GPP | 3DL | France, Germany, Hong Kong, Italy, Netherlands, Singapore, Switzerland | 1A, 7A, 8A | - | - | V1.0
CA_1A-7C | 3GPP | 3DL | Australia, UK | 1A, 7A | 7C | - | V1.0
CA_1A-8A-38A | 3GPP | 3DL | Singapore | 1A, 8A, 38A | - | - | V1.0

## Slide 10
CA_3A-20A-41A |  | 3DL |  | 3A, 20A | - | - | V1.0
CA_3A-28A-40A | 3GPP | 3DL | Australia, Saudi | 3A, 28A | - | - | V1.0
CA_3A-40C | 3GPP | 3DL | Australia, Hong Kong, Saudi | 3A | - | - | V1.0
CA_3A-41C | 3GPP | 3DL | Japan | 3A | - | - | V1.1
CA_3A-7A-20A | 3GPP | 3DL | UK, Spain, Germany, Italy, Switzerland | 3A, 7A, 20A | - | - | V1.0
CA_3A-7A-28A | 3GPP | 3DL | Australia, Germany, Netherlands, Switzerland, Taiwan | 3A, 7A, 28A | - | - | V1.0
CA_3A-7A-40A |  | 3DL |  | 3A, 7A | - | - | V1.0
CA_3A-7A-8A | 3GPP | 3DL | Hong Kong, Singapore, Taiwan | 3A, 7A, 8A | - | - | V1.0
CA_3A-7C | 3GPP | 3DL | Australia, Finland, Netherlands, UK | 3A, 7A | 7C | - | V1.0
CA_3A-8A-38A | 3GPP | 3DL | Singapore | 3A, 8A | - | - | V1.0
CA_3A-8A-41A | 3GPP | 3DL | . | 3A, 8A | - | - | V1.0
CA_3C-20A | 3GPP | 3DL | Germany, Switzerland | 3A, 20A | 3C | - | V1.0
CA_3C-28A | 3GPP | 3DL | Australia, Saudi | 3A, 28A | 3C | - | V1.0
CA_3C-38A | 3GPP | 3DL | Singapore | 3A | 3C | - | V1.0
CA_3C-5A | 3GPP | 3DL | Australia | 3A, 5A | 3C | - | V1.0
CA_3C-7A | 3GPP | 3DL | Australia, Singapore, UK | 3A, 7A | 3C | - | V1.0
CA_3C-8A | 3GPP | 3DL | Singapore, Korea | 3A, 8A | 3C | - | V1.0
CA_7A-28A-40A |  | 3DL |  | 7A, 28A | - | - | V1.0
CA_7C-20A | 3GPP | 3DL | UK | 7A, 20A | 7C | - | V1.0
CA_7A-40C |  | 3DL |  | 7A | - | - | V1.0
CA_7C-28A | 3GPP | 3DL | Australia, Brazil | 7A, 28A | 7C | - | V1.0
CA_8A-40C | 3GPP | 3DL | Hong Kong | 8A | - | - | V1.0
CA_8A-41C | 3GPP | 3DL | . | 8A | - | - | V1.0
CA_28A-40C | 3GPP | 3DL | Australia, Saudi | 28A | - | - | V1.0
CA_40D | 3GPP | 3DL | Australia, China Mainland, India, Thailand, Philippines | 40A | 40C | - | V1.0
CA_41D | 3GPP | 3DL | China Mainland, Japan, US, Philippines, Mexico | 41A | 41C | - | V1.0
CA_4A-7C | 3GPP | 3DL | UK, Spain, Germany, Italy, Switzerland | 4A,7A | 7C | - | V1.3
CA_7A-66A-66A | 3GPP | 3DL | Australia, Hong Kong, Saudi | 7A,66A | - | - | V1.3
CA_5A-7C | 3GPP | 3DL | Japan, Saudi | 7A,5A | 7C | - | V1.3
CA_2A-7C | 3GPP | 3DL | UK, Spain, Germany, Italy, Switzerland | 2A,7A | 7C | - | V1.3
CA_2A-4A-7A | 3GPP | 3DL | Australia, Brazil, Japan, Taiwan, Saudi | 2A,7A,4A | - | - | V1.3
CA_2A-4A-28A | 3GPP | 3DL | China Mainland, Korea | 2A,4A,28A | - | - | V1.3
CA_2A-7A-7A | 3GPP | 3DL | US | 2A,7A | - | - | V1.3
CA_2A-7A-28A | 3GPP | 3DL | US | 2A,7A,28A |  | - | V1.3
CA_3A-3A-28A | 3GPP | 3DL | UK, Spain, Germany, Italy, Switzerland | 3A,28A | - | - | V1.3
CA_3A-3A-7A | 3GPP | 3DL | Argentina, Australia, Brazil, Chile, Peru, Taiwan | 3A,7A | - | - | V1.3
CA_1A-3A-3A |  | 3DL |  | 3A,1A | - | - | V1.3
CA_1A-1A-28A | 3GPP | 3DL | Australia, Germany, Hong Kong, Singapore, Taiwan | 28A,1A | - | - | V1.3
CA_1A-1A-7A | 3GPP | 3DL | Australia, Canada | 7A,1A | - | - | V1.3
CA_1A-1A-3A | 3GPP | 3DL | Australia, Canada, Mexico, Peru, UK | 3A,1A |  | - | V1.3
CA_7A-28A-40A | 3GPP | 3DL | Taiwan | 7A,28A | - | - | V1.3

## Slide 11: EN-DC Combination

## Slide 12
Mode | NR | Sub-Category | CA & EN-DC Combination | 4G DL 2 × 2 MIMO | NR DL 4 × 4 MIMO | Sub-6 GHz Single UL/ UL MIMO |  |  | Sub-6 GHz ULCA | Spreadsheet Version
 |  |  |  |  |  | 4G UL | NR UL | 2 × 2 UL MIMO | NR UL | 
EN-DC | FDD | 1DL + FR1 | DC_28A_n1A | 28A | n1A | 28A | n1A | - | - | V1.0
EN-DC | FDD | 1DL + FR1 | DC_1A_n3A | 1A | n3A | 1A | n3A | - | - | V1.0
EN-DC | FDD | 1DL + FR1 | DC_8A_n3A | 8A | n3A | 8A | n3A | - | - | V1.0
EN-DC | FDD | 1DL + FR1 | DC_1A_n7A | 1A | n7A | 1A | n7A | - | - | V1.0
EN-DC | FDD | 1DL + FR1 | DC_3A_n7A | 3A | n7A | 3A | n7A | - | - | V1.0
EN-DC | FDD | 1DL + FR1 | DC_20A_n7A | 20A | n7A | 20A | n7A | - | - | V1.0
EN-DC | FDD | 1DL + FR1 | DC_28A_n7A | 28A | n7A | 28A | n7A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_1A_n38A | 1A | n38A | 1A | n38A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_3A_n38A | 3A | n38A | 3A | n38A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_1A_n78A | 1A | n78A | 1A | n78A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_3A_n78A | 3A | n78A | 3A | n78A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_7A_n78A | 7A | n78A | 7A | n78A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_8A_n78A | 8A | n78A | 8A | n78A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_20A_n78A | 20A | n78A | 20A | n78A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_28A_n78A | 28A | n78A | 28A | n78A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_38A_n78A | 38A | n78A | 38A | n78A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_1A_n79A | 1A | n79A | 1A | n79A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_3A_n79A | 3A | n79A | 3A | n79A | - | - | V1.0
EN-DC | FDD | 1DL + FR1 | DC_3A_n1A | 3A | n1A | 3A | n1A | - | - | V1.0
EN-DC | FDD | 1DL + FR1 | DC_7A_n1A | 7A | n1A | 7A | n1A | - | - | V1.0
EN-DC | FDD | 1DL + FR1 | DC_8A_n1A | 8A | n1A | 8A | n1A | - | - | V1.0
EN-DC | FDD | 1DL + FR1 | DC_20A_n1A | 20A | n1A | 20A | n1A | - | - | V1.0
EN-DC | FDD | 1DL + FR1 | DC_7A_n3A | 7A | n3A | 7A | n3A | - | - | V1.0
EN-DC | FDD | 1DL + FR1 | DC_20A_n3A | 20A | n3A | 20A | n3A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_1A_n77A | 1A | n77A | 1A | n77A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_3A_n77A | 3A | n77A | 3A | n77A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_28A_n77A | 28A | n77A | 28A | n77A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_3A_n41A | 3A | n41A | 3A | n41A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_8A_n41A | 8A | n41A | 8A | n41A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_1A_n40A | 1A | n40A | 1A | n40A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_3A_n40A | 3A | n40A | 3A | n40A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_20A_n40A | 20A | n40A | 20A | n40A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_28A_n40A | 28A | n40A | 28A | n40A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_40A_n78A | 40A | n78A | 40A | n78A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_20A_n41A | 20A | n41A | 20A | n41A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_1A_n41A | 1A | n41A | 1A | n41A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_41A_n78A | 41A | n78A | 41A | n78A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_28A_n41A | 28A | n41A | 28A | n41A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_5A_n40A | 5A | n40A | 5A | n40A | - | - | V1.0
EN-DC | TDD | 1DL + FR1 | DC_8A_n38A | 8A | n38A | 8A | n38A | - | - | V1.0

## Slide 13
EN-DC | TDD | 1DL + FR1 | DC_2A_n78A | 2A | n78 | 2A | n78A | - | - | V1.3
EN-DC | TDD | 1DL + FR1 | DC_4A_n78A | 4A | n78 | 4A | n78A | - | - | V1.3
EN-DC | TDD | 1DL + FR1 | DC_7A_n40A | 7A | n40 | 7A | n40 | - | - | V1.3
EN-DC | FDD | 1DL + FR1 | DC_7A_n28A | 7A | n28 | 7A | n28 | - | - | V1.3
EN-DC | FDD | 1DL + FR1 | DC_2A_n28A | 2A | n28 | 2A | n28 | - | - | V1.3
EN-DC | FDD | 1DL + FR1 | DC_ 28A_n1A | 28A | n1 | 28A | n1 | - | - | V1.3
EN-DC | FDD | 1DL + FR1 | DC_66A_n7A | 66A | n7 | 66A | n7 | - | - | V1.3
EN-DC | FDD | 1DL + FR1 | DC_2A_n7A | 2A | n7 | 2A | n7 | - | - | V1.3
EN-DC | TDD | 1DL + FR1 | DC_66A_n78A | 66A | n78 | 66A | n78A | - | - | V1.3
EN-DC | FDD | 2DL + FR1 | DC_3A-8A_n1A | 3A-8A, 8A-3A | n1A | 3A, 8A | n1A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_3A-28A_n1A | 3A-28A, 28A-3A | n1A | 3A, 28A | n1A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_3A-41A_n1A | 3A-41A | n1A | 3A | n1A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_7A-8A_n1A | 7A-8A, 8A-7A | n1A | 7A, 8A | n1A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_7A-28A_n1A | 7A-28A, 28A-7A | n1A | 7A, 28A | n1A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_1A-8A_n3A | 1A-8A, 8A-1A | n3A | 1A, 8A | n3A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_7A-8A_n3A | 7A-8A, 8A-7A | n3A | 7A, 8A | n3A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_1A-3A_n7A | 1A-3A, 3A-1A | n7A | 1A, 3A | n7A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_1A-8A_n7A | 1A-8A, 8A-1A | n7a | 1A, 8A | n7A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_1A-20A_n7A | 1A-20A, 20A-1A | n7a | 1A, 20A | n7A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_1A-28A_n7A | 1A-28A, 28A-1A | n7A | 1A, 28A | n7A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_1A-40A_n7A | 1A-40A | n7A | 1A | n7A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_3A-20A_n7A | 3A-20A, 20A-3A | n7A | 3A, 20A | n7A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_3A-28A_n7A | 3A-28A, 28A-3A | n7A | 3A, 28A | n7A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_3A-40A_n7A | 3A-40A | n7A | 3A | n7A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3C_n78A | 3C | n78A | 3C | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_7C_n78A | 7C | n78A | 7C | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-3A_n78A | 1A-3A, 3A-1A | n78A | 1A, 3A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-7A_n78A | 1A-7A, 7A-1A | n78A | 1A, 7A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-8A_n78A | 1A-8A, 8A-1A | n78A | 1A, 8A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-20A_n78A | 1A-20A, 20A-1A | n78A | 1A, 20A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-3A_n78A | 3A-3A | n78A | 3A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-7A_n78A | 3A-7A, 7A-3A | n78A | 3A, 7A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-8A_n78A | 3A-8A, 8A-3A | n78A | 3A, 8A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-20A_n78A | 3A-20A, 20A-3A | n78A | 3A, 20A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-28A_n78A | 3A-28A, 28A-3A | n78A | 3A, 28A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-38A_n78A | 3A-38A | n78A | 3A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_7A-20A_n78A | 7A-20A, 20A-7A | n78A | 7A, 20A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_7A-28A_n78A | 7A-28A, 28A-7A | n78A | 7A, 28A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_7A-40A_n78A | 7A-40A | n78A | 7A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_8A-41A_n78A | 8A-41A | n78A | 8A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_20A-38A_n78A | 20A-38A | n78A | 20A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_20A-40A_n78A | 20A-40A | n78A | 20A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_20A-41A_n78A | 20A-41A | n78A | 20A | n78A | - | - | V1.0

## Slide 14
EN-DC | FDD | 2DL + FR1 | DC_3A-20A_n1A | 3A-20A, 20A-3A | n1A | 3A, 20A | n1A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_3A-7A_n1A | 3A-7A | n1A | 3A, 7A | n1A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_7A-20A_n1A | 7A-20A, 20A-7A | n1A | 7A, 20A | n1A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_1A-20A_n3A | 1A-20A, 20A-1A | n3A | 1A, 20A | n3A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_1A-7A_n3A | 1A-7A, 7A-1A | n3A | 1A, 7A | n3A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-3A_n77A | 1A-3A, 3A-1A | n77A | 1A, 3A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-7A_n77A | 1A-7A, 7A-1A | n77A | 1A, 7A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-8A_n77A | 1A-8A, 8A-1A | n77A | 1A, 8A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-20A_n77A | 1A-20A, 20A-1A | n77A | 1A, 20A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-28A_n77A | 1A-28A, 28A-1A | n77A | 1A, 28A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-40A_n77A | 1A-40A | n77A | 1A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-41A_n77A | 1A-41A | n77A | 1A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-41A_n78A | 1A-41A | n78A | 1A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-8A_n77A | 3A-8A, 8A-3A | n77A | 3A, 8A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-20A_n77A | 3A-20A, 20A-3A | n77A | 3A, 20A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-28A_n77A | 3A-28A, 28A-3A | n77A | 3A, 28A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-40A_n77A | 3A-40A | n77A | 3A | n77A |  |  | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-41A_n77A | 3A-41A | n77A | 3A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-41A_n78A | 3A-41A | n78A | 3A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_7A-7A_n78A | 7A-7A | n78A | 7A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-28A_n40A | 1A-28A, 28A-1A | n40A | 1A, 28A | n40A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-3A_n40A | 1A-3A, 3A-1A | n40A | 1A, 3A | n40A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-7A_n40A | 1A-7A, 7A-1A | n40A | 1A, 7A | n40A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-8A_n40A | 1A-8A, 8A-1A | n40A | 1A, 8A | n40A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-20A_n40A | 1A-20A, 20A-1A | n40A | 1A, 20A | n40A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-7A_n40A | 3A-7A, 7A-3A | n40A | 3A,7A | n40A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-20A_n40A | 3A-20A, 20A-3A | n40A | 3A, 20A | n40A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-28A_n40A | 3A-28A, 28A-3A | n40A | 3A, 28A | n40A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-40A_n78A | 1A-40A | n78A | 1A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_28A-40A_n78A | 28A-40A | n78A | 28A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-40A_n78A | 3A-40A | n78A | 3A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-28A_n78A | 1A-28A, 28A-1A | n78A | 1A, 28A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_40C_n78A | 40C | n78A | 40A, 40C | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_41A-41A_n78A | 41A-41A | n78A | 41A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_41C_n78A | 41C | n78A | 41A, 41C | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_7A-8A_n78A | 7A-8A, 8A-7A | n78A | 7A, 8A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-3A_n41A | 1A-3A, 3A-1A | n41A | 1A, 3A | n41A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-8A_n41A | 1A-8A, 8A-1A | n41A | 1A, 8A | n41A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-20A_n41A | 1A-20A, 20A-1A | n41A | 1A, 20A | n41A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1A-28A_n41A | 1A-28A, 28A-1A | n41A | 1A, 28A | n41A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_3A-3A_n7A | 3A-3A | n7A | 3A | n7A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_3A-3A_n1A | 3A-3A | n1A | 3A | n1A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_7A-7A_n1A | 7A-7A | n1A | 7A | n1A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_7A-40A_n1A | 7A-40A | n1A | 7A | n1A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_7A-7A_n40A | 7A-7A | n40A | 7A | n40A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-3A_n40A | 3A-3A | n40A | 3A | n40A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_7A-8A_n40A | 7A-8A, 8A-7A | n40A | 7A, 8A | n40A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_7A-20A_n40A | 7A-20A, 20A-7A | n40A | 7A, 20A | n40A | - | - | V1.0

## Slide 15
EN-DC | TDD | 2DL + FR1 | DC_7A-28A_n40A | 7A-28A, 28A-7A | n40A | 7A, 28A | n40A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-3A_n77A | 3A-3A | n77A | 3A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-7A_n77A | 3A-7A, 7A-3A | n77A | 3A, 7A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_7A-7A_n77A | 7A-7A | n77A | 7A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_7A-8A_n77A | 7A-8A, 8A-7A | n77A | 7A, 8A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_7A-20A_n77A | 7A-20A, 20A-7A | n77A | 7A, 20A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_7A-28A_n77A | 7A-28A, 28A-7A | n77A | 7A, 28A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_7A-40A_n77A | 7A-40A | n77A | 7A | n77A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-3A_n41A | 3A-3A | n41A | 3A | n41A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-8A_n41A | 3A-8A, 8A-3A | n41A | 3A, 8A | n41A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-20A_n41A | 3A-20A, 20A-3A | n41A | 3A, 20A | n41A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-28A_n41A | 3A-28A, 28A-3A | n41A | 3A, 28A | n41A | - | - | V1.0
EN-DC | FDD | 2DL + FR1 | DC_3A-40A_n1A | 3A-40A | n1A | 3A | n1A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_1C_n78A | 1C | n78A | 1A | n78A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_3A-8A_n40A | 3A-8A, 8A-3A | n40A | 3A, 8A | n40A | - | - | V1.0
EN-DC | TDD | 2DL + FR1 | DC_66A-66A_n78A | 66A-66A | n78 | 66A | n78A | - | - | V1.3
EN-DC | TDD | 2DL + FR1 | DC_7A-66A_n78A | 66A-7A,7A-66A | n78 | 66A,7A | n78A | - | - | V1.3
EN-DC | TDD | 2DL + FR1 | DC_5A-7A_n78A | 5A-7A,7A-5A | n78 | 5A,7A | n78A | - | - | V1.3
EN-DC | TDD | 2DL + FR1 | DC_5A-66A_n78A | 5A-66A,66A-5A | n78 | 5A,66A | n78A | - | - | V1.3
EN-DC | TDD | 2DL + FR1 | DC_2A-7A_n78A | 2A-7A,7A-2A | n78 | 2A,7A | n78A | - | - | V1.3
EN-DC | TDD | 2DL + FR1 | DC_2A-38A_n78A | 2A-38A | n78 | 2A | n78A | - | - | V1.3
EN-DC | TDD | 2DL + FR1 | DC_2A-66A_n78A | 2A-66A,66A-2A | n78 | 2A,66A | n78A | - | - | V1.3
EN-DC | TDD | 2DL + FR1 | DC_2A-28A_n78A | 2A-28A,28A-2A | n78 | 2A,28A | n78A | - | - | V1.3
EN-DC | FDD | 2DL + FR1 | DC_7C_n28A | 7A,7C | n28 | 7A,7C | n28 | - | - | V1.3
EN-DC | FDD | 2DL + FR1 | DC_ 7C_n1A | 7C,7A | n1 | 7A,7C | n1 | - | - | V1.3
EN-DC | FDD | 2DL + FR1 | DC_3C_n1A | 3A,3C | n1 | 3A,3C | n1 | - | - | V1.3
EN-DC | FDD | 2DL + FR1 | DC_66A-66A_n7A | 66A-66A | n7 | 66A-66A | n7 | - | - | V1.3
EN-DC | TDD | 3DL + FR1 | DC_1A-3C_n41A | 1A-3C, 3C-1A | n41A | 1A,3A | n41A | - | - | V1.0
EN-DC | TDD | 3DL + FR1 | DC_1A-3C_n78A | 1A-3C, 3C-1A | n78A | 1A, 3C | n78A | - | - | V1.0
EN-DC | TDD | 3DL + FR1 | DC_1A-7C_n78A | 1A-7C, 7C-1A | n78A | 1A, 7C | n78A | - | - | V1.0
EN-DC | TDD | 3DL + FR1 | DC_3A-7C_n78A | 3A-7C, 7C-3A | n78A | 3A, 7C | n78A | - | - | V1.0
EN-DC | TDD | 3DL + FR1 | DC_3C-7A_n78A | 7A-3C, 3C-7A | n78A | 3C, 7A | n78A | - | - | V1.0
EN-DC | TDD | 3DL + FR1 | DC_3C-20A_n78A | 3C-20A, 20A-3C | n78A | 3C, 20A | n78A | - | - | V1.0
EN-DC | TDD | 3DL + FR1 | DC_1A-41C_n78A | 1A-41C | n78A | 1A | n78A | - | - | V1.0
EN-DC | TDD | 3DL + FR1 | DC_3C-28A_n78A | 3C-28A, 28A-3C | n78A | 3C, 28A | n78A | - | - | V1.0
EN-DC | TDD | 3DL + FR1 | DC_7C-28A_n78A | 7C-28A, 28A-7C | n78A | 7C, 28A | n78A | - | - | V1.0
EN-DC | TDD | 3DL + FR1 | DC_1A-28C_n41A | 1A-28C, 28C-1A | n41A | 1A, 28C | n41A | - | - | V1.0
EN-DC | TDD | 3DL + FR1 | DC_3A-28C_n41A | 3A-28C, 28C-3A | n41A | 3A, 28C | n41A | - | - | V1.0
EN-DC | TDD | 3DL + FR1 | DC_3C-8A_n41A | 3C-8A, 8A-3C | n41A | 3C, 8A | n41A | - | - | V1.0
EN-DC | TDD | 3DL + FR1 | DC_3C-20A_n41A | 3C-20A, 20A-3C | n41A | 3A, 20A | n41A | - | - | V1.0
EN-DC | TDD | 3DL + FR1 | DC_3C-20A_n77A | 3C-20A, 20A-3C | n77A | 3A, 20A | n77A | - | - | V1.0
EN-DC | TDD | 3DL + FR1 | DC_3C-28A_n77A | 3C-28A, 28A-3C | n77A | 3A, 28A | n77A | - | - | V1.0
EN-DC | TDD | 3DL + FR1 | DC_7C-66A_n78A | 66A-7C,7C-66A | n78 | 66A,7A,7C | n78A | - | - | V1.3
EN-DC | TDD | 3DL + FR1 | DC_2A-7C_n78A | 2A-7C,7C-2A | n78 | 2A,7A,7C | n78A | - | - | V1.3